Operation Manual

PREDATOR PLATINUM

TURNTABLE STRETCH WRAPPER

SERIAL NUMBER

Please refer to the serial number in all correspondence with Highlight or any Highlight Distributor. This identifies your machine and will help in our ability to quickly and efficiently respond to your needs.

OPERATION MANUAL NUMBER: PRED_PLATINUM / MAY-2013

Table of Contents

Table of Contents	1

Table of Figures	2

General Information	3

Safety Messages	4

Introduction and Warranty	6

Revision History	8

Specifications	9

Specifications	10

System Overview Prints	12

Installation & Adjustments	14

Machine Placement	15

Machine Set-Up	16

Pre-Stretch Adjustment	18

Frequency Drive Adjustments	21

Optional Height Detection Sensor	32

Load Compression Testing	33

Optional Scale Package	34

Operation Instructions	37

Operator Controls	38

Film Loading	43

Machine Operating Instructions	44

Film Cutting	46

Maintenance	47

Preventative Maintenance	48

Maintenance Schedule	51

Trouble-shooting	52

Troubleshooting Guide	53

Power Problems	54

Turntable Problems	55

Film Carriage Problems	57

Film Delivery Problems	59

Film Cutting Problems ...….…………………………………………………………………....62

Technical References	63

Recommended Spare Parts	64

Electrical Drawings	65

Mechanical Drawings	78

Pneumatic Drawings ....................................................................................................... 93

Notes	96

Table of Figures

Figure 1: Predator Platinum Low Profile, Overview Layout	12

Figure 2: Predator Platinum Low Profile Machine Description	13

Figure 3: Ramp Positioning for Predator Platinum Low Profile	16

Figure 4: Pre-Stretch Percentage Gear Set Swap	20

Figure 5: Altivar 12 AC Drive Keypad	21

Figure 6: Ultrasonic Sensing Concept	32

Figure 7: Operator Panel 	43

Figure 8: Film Loading/Threading Diagram……………………………………………………..43

Figure 8: Turntable Belt Adjustment	49

Figure 9: Film Carriage Lift Chain Adjustment	50

1

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

General
Information

Safety Messages

For the best result with the Predator Platinum Turntable Stretch Wrapper, carefully read this manual and all of the warning labels attached to the equipment before installing and operating it, and follow instructions exactly. Keep this manual for machine reference.

Definitions and Symbols

High Voltage!

This symbol indicates high voltage. It calls your attention to items or operations that could be dangerous to you or other persons operating the equipment. Read the message and follow the instructions carefully.

Warning!

This symbol indicates a potentially hazardous situation which, if not avoided, can result to bodily injury, or serious damage to the product.

Notes

This symbol indicates an area or subject of special merit, emphasizing the equipment’s capabilities, common errors in operation or maintenance, or other special instructions that can provide benefits to users.

General Precautions – Read These First!

High Voltage!

Disconnect AC input power before checking components, performing maintenance, cleaning up, and when the machine is not in use. Do NOT connect or disconnect wires and connectors while power is applied to circuit.

High Voltage!

Wiring work should be carried out only by qualified personnel. Otherwise, there is a danger of electric shock or fire.

High Voltage!

The user is responsible for conforming to all applicable code requirements with respect to grounding all requirements. Do NOT use extension cords to operate the equipment.

High Voltage!

Motor control equipment and electronic controllers are connected to hazardous line voltages. When servicing drives and controllers, there may be exposed components with housings or protrusions at or above line potential. Extreme care should be taken to protect against shock.

Warning!

Loose clothing must NOT be worn while the machine is in operation. Stay clear of moving parts while the machine is running.

Introduction and Warranty

Introduction

Thank you for your purchase of a Predator Platinum Turntable Stretch Wrapper! Designed for the high volume industrial user, the Predator Platinum will stretch wrap any load to the maximum stretch level of any film with full independent control of the film force. This allows even light unstable loads to be wrapped at lower cost and maximum load holding force.

Limited Warranty

Highlight Industries, Inc. warrants its Predator manufactured by it, and sold pursuant to this order, will be of merchantable quality, free from defects in material and workmanship as determined at the date of shipment, by generally recognized, applicable and accepted practices and procedures in the industry, for a period of three (3) years from the Highlight invoice date, under normal use and service.

When the Purchaser gives Highlight written notice of any alleged defect within the applicable warranty period, Highlight will, at its option repair or replace the same free of charge F.O.B. its manufacturing plant, installation not included.  Equipment replaced under the warranty shall have the same warranty as new equipment but does not extend the warranty of the original equipment.

Satisfaction of this warranty, consistent with other provisions herein, will be limited to the replacement or repair or modification of, or issuance of a credit for, the equipment involved, at Highlight’s option.

Highlight neither assumes nor authorizes any person to assume for it any other obligation in connection with the sale of Highlight’s equipment.

This warranty shall not apply to any equipment which has been repaired or altered by un-authorized personnel in any way so as to, in the judgment of Highlight, affect serviceability, or which has been subjected to misuse, negligence, accident, or to equipment made by Highlight which has been operated in a manner contrary to Highlight’s instructions.

In no event regardless of the cause, shall Highlight be liable for penalties or penalty clauses of any description or any damages resulting from loss of profits, use of products or for any incidental indirect or consequential damages, even if advised of the possibility of such damages. This limitation of Highlight’s liability will apply regardless of the form of action, whether in contract or tort, including negligence.  Any action against Highlight must be brought within twelve (12) months after cause of action accrues.

“This warranty in lieu of all other warranties whether expressed, implied or statutory including implied warranties of merchantability of fitness or extends only to the buyer or customer purchasing from Highlight Industries, Inc or an authorized distributor.”

About This Document

The purpose of this manual is to provide you with information necessary to install, operate, troubleshoot, and maintain the Predator Platinum Turntable Stretch Wrapper. The audience for this manual should have basic knowledge of mechanical and electronic components, standard electrical wiring practices, and schematics symbols.

To guarantee safe operation of the equipment, carefully observe the safety messages throughout this manual. Keep this operating manual and distribute it to all users for reference.

Application Assistance

If any assistance is desired, contact the distributor from whom you have purchased the unit, or call the number listed on the bottom of each page of this manual. To receive quick and proper technical support for the equipment you have purchased, please be prepared to provide the following information:

- Machine Serial Number

- Date of Purchase

- Symptoms of any problems

Revision History

| Revision | Revision Comment | Date of Revision |
| --- | --- | --- |
|  | Initial Release | January 2011 |
| 1 | Changed hot wire from, turntable bearing, and turntable bearing plate. | May 2011 |
| 2 | Updated turntable brake parts, pneumatic parts, and added scale information. | August 2011 |
| 3 | Updated wiper parts to include bearing upgrade. | February 2012 |
| 4 | Updated carriage limit switches. | November 2012 |
| 5 | Updated frequency drives. | May 2013 |
| 6 | 306532 was 300041, added film ringer assembly | Jul 2013-RDU |
| 7 | Added compressed air requirements | Nov 2013-RDU |
| 8 | Added wiper/jaw rod end part numbers. | Dec 2013-RDU |

2

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

Specifications

Specifications

Machine Dimensions

| Length (inch) | 113 |
| --- | --- |
| Width (inch) | 71 |
| Height (inch) | 92 |
| Turntable Height from Floor (inch) | 3.5 |
| Wrapping Height (inch) | 80 |
| Turntable Diameter (inch) | 70 |
| Operation Space (inch) | 105 x 70 x 100 |
| Maximum Pallet Size (inch) | 48 x 48 x 80 |
| Shipping Weight (lbs) | 1500 |

Electrical Specifications

- 120VAC, 60Hz, Single Phase, 15Amp

- Lockable Disconnect Switch

- Operating temperature: +32°F to +110°F

- NEC wiring standard

- Industrial NEMA-12 rated electrical panel

- Programmable Logic Controller (PLC) with input/output diagnostic lights

Turntable

- 4,400 lbs Maximum Turntable Load Capacity

- 12 RPM Maximum Turntable Speed

- 30-40 Loads Per Hour

- 1 HP 3-Phase AC Motor with 1 HP AC Frequency Drive

Film Carriage

- Adjustable Speed

- Automatic Package Height Detection

- 1/2 HP 3-Phase AC Motor

- 1/2 HP AC Frequency Drive

Pneumatic Requirements

- 80psi, 3SCFM clean dry air

Film Delivery

- Fixed Selectable 200% / 250% Average Pre-Stretch Level (Optional 230% / 300%)

- Adjustable Film Force

- 10 Inch Diameter Roll Capacity

- 20 Inch Height Roll Capacity

- 1/4 HP 3-Phase AC Motor

- 1/2 HP AC Frequency Drive

| Part Number | Description | Number of Teeth |
| --- | --- | --- |
| 301339 | Drive Gear | 17 |
| 301340 | Lower Fixed Gear | 46 |
| 301341 | Upper Fixed Gear | 42 |
| 301342 | Slip Gear | 46/42 |

System Overview Prints

Note

Shown below are STANDARD assembly drawings. It may not reflect your purchased system, especially when optional items are added. Refer to the Technical References section of the manual for more detailed information.

Figure 1: Predator Platinum Low Profile, Overview Layout

System Description

Figure 2: Predator Platinum Low Profile Machine Description

3

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation  Manual

Installation & Adjustments

Machine Placement

Receiving and Inspections

The Predator Platinum Turntable Stretch Wrapper has gone through quality control tests at the factory before shipment. Upon receiving, please do the following:

- Inspect the entire machine for visual damage during shipment. If found, immediately report this damage to the trucking line. Highlight Industries, Inc. has taken every precaution during the packaging and loading of this equipment, however, it is YOUR RESPONSIBILITY to inspect for damage before installation.

- Make sure the part or serial number indicated on the machine corresponds with the part number of your order.

Positioning of the Machine

Place the Predator Platinum Turntable Stretch Wrapper close to an area where you will be wrapping your loads. Make sure that there is sufficient room to load/unload the machine and that you do not stretch the power cable. Remember, you will need to plug the machine in to a 120VAC, 15-Amp outlet and supply clean dry compressed air.

Floor Weight Bearing/Stress Tolerance

The floor must be able to bear the weight of the machine, the weight of the maximum load, plus a safety factor. The floor must also be able to tolerate the stress of the machine’s operation. If the fork trucks will operate on the same weight bearing area, add the weight of the trucks to the weight bearing stress tolerance requirements.

The Predator Platinum can be installed on any type of floor constructions that meets the weight bearing and stress tolerance requirements.

Warning!

The Predator Platinum must be anchored securely to the floor, using the type of anchor recommended for your floor.

Machine Set-Up

Unpacking and Moving the Machine

It is very important to read all instructions before undertaking any of these steps. The following steps should help achieving a safe and quick machine set-up.

- Place the skidded machine close to the designated wrap area. Remove all shipping fasteners holding the machine to the pallet.

- Place the forks of the forklift through the tubes provided on the base of the machine, remove the machine from the shipping skids, and place it in the designated wrap area.

- Supply 80psi, 3SCFM clean dry compressed air to the filter regulator on the side of the tower.

- If the OPTIONAL ramp (Part Number #600086) is purchased: Select a ramp position as illustrated below. The ramp can be positioned anywhere in a 180° rotation around the front of the turntable. There should be a ¼” gap between the turntable and the ramp. The ramp should be fully supported by the floor. Both the ramp and the machine should be lagged to the floor.

Warning!

It is very important that the machine be leveled. Uneven floors will cause premature turntable support roller failure.

Figure 3: Ramp Positioning for Predator Platinum Low Profile

Power and Control Wiring Checks

- Using a volt meter, check the AC voltage coming to the machine and insure the proper voltage is present.

- Make sure the Emergency Stop button on the operator panel is fully pressed in. Turn the disconnect switch to the ON position.

- Pull the Emergency Stop button out. Power should now be applied to the AC frequency drives, PLC, photo-electric sensors, switches, and LED’s. Press the Emergency Stop button again and ensure that power to the Frequency Drives is removed.

- Open the film carriage door. Make sure all machine power is completely removed when the carriage door is open. Close the film carriage door to resume.

- Open the electrical control box. Make sure all machine power is completely removed when the electrical control box is open. Close the electrical control box to resume.

- Trip the carriage foot security bar. Make sure all machine power is completely removed when the carriage foot security bar is tripped. Clear the bar to resume.

PLC Input Checks

- Open the electrical control box, and insert the key latch onto the safety door switch.

- Depress push buttons and activate selector switches on the operator panel, check for each corresponding input lights on the front face of PLC.

- Block the “Product Height Detection” photoelectric sensor (located on the film carriage), check for corresponding input light on the front face of PLC.

- Trigger magnetic proximity and limit switch sensors, check each corresponding input lights on the front face of the PLC.

- Remove the key latch, and close the electrical control box to resume.

Warning!

Do NOT remove or modify the fixed upper and lower Film Carriage limit switch stops.

Pre-Stretch Adjustment

Pre-Stretch Percentage Change

To change the pre-stretch percentage, follow the procedure below:

- Turn the main disconnect switch off.

- Remove the knob cover on the film carriage.

- Push the safety lock and slide the knob to change the pre-stretch percentage. Lift the knob for the high percentage, or lower the knob for low percentage. Standard percentages are 200% (low) and 250% (high).

- To insure safety and correct operation of the stretch gears, check the following items:

  - The safety line is back to its home position following the profile of the knob.

  - The light indicates the selected pre-stretch percentage.

Replacing Pre-Stretch Percentage Gear Set

To swap the pre-stretch percentage gear set, follow the illustration below:

Figure 4: Pre-Stretch Percentage Gear Set Swap

Frequency Drive Adjustments

An AC Frequency Drive is a device that controls the 3-phase AC motor’s speed by varying the frequency and voltage sent to the motor. The Predator Platinum Turntable Stretch Wrapper uses Schneider Electric Altivar 12 Adjustable Frequency Drives. Refer to the Electrical Schematic Drive Parameters Technical References section for detailed drive parameter settings. Refer to the drive manufacturer’s manual for more detailed drive information.

Altivar 12 Digital Keypad Description

The digital keypad includes the displays panel and the keypad. The display panel provides the parameter display and shows the operation status of the AC drive. The keypad provides programming and control interface.

Figure 5: Altivar 12 AC Drive Keypad

Keypad Description:

- Value LED. When illuminated it indicates when a numeric value is being displayed.

- Charge LED. When illuminated it indicates when drive capacitors are fully charged.

- Unit LED. When illuminated it indicates when a unit, such as AMPS, is being displayed.

- ESC button. Exits a menu or parameter, or aborts the displayed value and returns to the previous value in the memory.

- STOP button. Stops the motor. The run command will have to be cycled before the motor will be allowed to run again.

- RUN button. Starts running the motor if the drive is configured for control by the drive keypad.

- Jog Dial. Used for navigation of the menus. Turn clockwise or counterclockwise to scroll through the menu list and is used for selection/validation when the dial is pressed.

- MODE button. Switches between the control/programming modes.

- CONFIGURATION mode LED. When illuminated it indicates when a value can be changed.

- MONITORING mode LED. When illuminated it indicates when the display is monitoring the current status of the drive.

- REFERENCE mode LED. When illuminated it indicates when the display is showing the speed reference value.

- Four 7-Segment displays. The display of the drive for menus and settings.

Menu Structure

To access the monitoring parameters, press the wheel on the face of the frequency drive. Using the wheel, scroll through the menu until the display shows Non (Mon) for monitoring mode. This gives the user access to all the monitoring parameters.

To access the complete set of drive parameters first press the wheel to access different modes. Using the wheel, scroll to “COnF” and press the wheel again; this will access different sets of parameters. Using the wheel, scroll to “FULL” and press the wheel; this will give the user access to the complete parameter set.

Monitoring Parameters

| Code | Name/Description | Unit |
| --- | --- | --- |
| LFr | External reference value: External keypad or local force mode configured. Forced local reference FLOC page 61 set to LCC and Forced local assignment FLO page 61 different to nO. Displays the speed reference coming from the remote keypad. This value is not visible in factory setting. | Hz |
| rFr | Output Frequency: This function provides the estimated motor speed. It corresponds to the estimated motor frequency (on the motor shaft). In Standard law the Output frequency rFr is equal to stator frequency. In Performance law the Output frequency rFr motor speed is equal to the estimated motor speed. Range: -400 to 400 Hz | Hz |
| LCr | Motor Current: Estimation of the effective motor current from phase current measurements with an accuracy of 5%. During DC injection, the current displayed is the maximum value of current injected in the motor. | A |
| ULn | Main Voltage: Line voltage from the point of view of the DC bus, motor running or stopped. | A |
| StAt | Product Status: rdY – Drive Ready rUn – Drive Running ACC – Acceleration in progress dEc – Deceleration in progress dCb – DC injection braking in progress CLi – Current limit nSt – Freewheel stop control Obr – Auto-Adapted deceleration CtL – Controlled stop on mains phase loss tUn – Auto-tuning in progress FSt – Fast stop active nLP – No line power | N/A |

Programming Functions

All functions have been Highlight factory set and tested. The factory settings listed in this manual are the drive manufacturer’s factory setting, not the Highlight Industries factory settings. Refer to the Electrical Schematic Drive Parameters page of the Technical References section for the Highlight factory settings. Some of the most commonly adjusted programmable functions (parameters) are listed below.

Note

Refer to the drive manufacturers Operation Manual or website for complete lists and explanations of the programming parameters.

I_O Menu

| Code | Sub-Code | Name/Description | Factory Setting |
| --- | --- | --- | --- |
| tCC |  | Type of Control: 2C – 2-wire control 3C – 3-wire control | 2C |
| AI1- | AI1t | Analog Input 1 Type: 5U – 0-5VDC input voltage 10U – 0-10VDC input voltage 0A – 0-20mA current input | 5U |
| r1 |  | Relay Output 1 Assignment: nO – Not assigned FLt – No error detected rUn – Drive run | FLt |
| AO1- | AO1 | Analog Output 1 Assignment: nO – Not Assigned OCr – Motor current OFr – Output Frequency | nO |
|  | AO1t | Analog Output 1 Type: 10U – 0-10VDC 0A – 0-20mA 4A – 4-20mA | 0A |

drC Menu

| Code | Sub-Code | Name/Description | Adjustment Range | Factory Setting |
| --- | --- | --- | --- | --- |
| bFr |  | Standard Motor Frequency | 50/60 | 50 Hz |
| nPr |  | Rated Motor Power (% of drive rated HP) | 0.5-1.2 | 1 |
| UnS |  | Rated Motor Voltage | 100-480V | 230V |
| nCr |  | Rated Motor Current | plate | Varies |
| FrS |  | Rated Motor Frequency | 10-400Hz | 50 Hz |
| nSP |  | Rated Motor Speed | 0-24000rpM | Varies |
| tFr |  | Maximum Frequency | 10-400Hz | 72 Hz |
| Ctt |  | Motor Control Type: PErF – Performance, Sensorless Vector Std – Standard, Volts/Hertz PUNP – Pump, low torque |  | Std |
| UFr |  | IR Compensation: Optimizes torque at very low speeds | 25-200% | 100% |
| SLP |  | Slip Compensation | 0-150% | 100% |
| StA |  | Frequency Loop Stability: Adjusts overshoots and oscillations at the end of acceleration or deceleration. A higher number decreases oscillations | 0-100% | 20% |
| FLG |  | Frequency Loop Gain: Adjusts the slope of the speed increase. A lower number decreases oscillations. | 0-100% | 20% |
| tUn |  | Motor Auto Tuning: Automatically tunes the drive to the motor profile | nO/YES/dOnE | nO |

CtL Menu

| Code | Sub-Code | Name/Description | Factory Setting |
| --- | --- | --- | --- |
| Fr1 |  | Speed Reference Channel 1: AI1 – Terminal analog input LCC – Remote Display Ndb – Modbus AIU1 – Jog dial (wheel) on drive | AI1 |
| CHCF |  | Channel Configuration: SIN – Not separate mode. Speed and run commands from the same source. SEP – Separate mode. Speed and run commands from different sources. | SIM |
| Cd1 |  | Command Channel 1 (run fwd/rev, stop): Only appears if CHCF is set to SEP. tEr – terminals LOC – Local LCC – Remote display Ndb – Modbus | tEr |

FUn Menu

| Code | Sub-Code | Name/Description | Adjustment Range | Factory Setting |
| --- | --- | --- | --- | --- |
| rPt- | ACC | Acceleration Time (seconds) | 0.0-999.9 s | 3.0 s |
|  | dEC | Deceleration Time (seconds) | 0.0-999.9 s | 3.0 s |
|  | brA | Decel Ramp Adaptation Assignment: nO – Function inactive. (Used with dynamic braking) YES – Automatically increases the deceleration time to prevent a DC bus overvoltage dYnA – Most rapid deceleration possible without a dynamic braking resistor. |  | YES |
| Stt- | Stt | Type of Stop: rNP – Ramp Stop FSt – Fast Stop nSt - Freewheel |  | rNP |
| rrS |  | Reverse Direction Assignment: nO – Function inactive L1H – Input L1 active high L2H – Input L2 active high L3H – Input L3 active high L4H – Input L4 active high |  | nO |
| AdC- | AdC | Automatic DC Injection: nO – function inactive YES – Time limited DC injection Ct – Continuous DC injection |  | YES |
|  | SdC1 | Automatic DC Injection Current | 0-120% if nCr | 70% |
|  | tdC1 | Automatic DC Injection Time (seconds) | 0.1-30 s | 0.5 s |
| PSS- | PS2 | Second Preset Speed Assignment: nO – Function inactive L1H – Input L1 active high L2H – Input L2 active high L3H – Input L3 active high L4H – Input L4 active high |  | nO |
|  | SP2 | Second Preset Speed Reference | 0-400 Hz | 10 Hz |
| CLI- | CL1 | Current Limitation | 0.25-1.5 plate | varies |
| SPL- | LSP | Low Speed Setting (Hz) | 0-HSP | 0 Hz |
|  | HSP | High Speed Setting (Hz) | LSP-tFr | 60 Hz |

FLt Menu

| Code | Sub-Code | Name/Description | Factory Setting |
| --- | --- | --- | --- |
| rSF |  | Fault Reset Assignment: nO – Function inactive L1H – Input L1 active high L2H – Input L2 active high L3H – Input L3 active high L4H – Input L4 active high | nO |
| Atr- | Atr | Automatic Restart: nO – Function inactive YES – Automatic drive restart after fault condition | nO |
|  | tAr | Max automatic restart time | 5 min |
| FLr |  | Flying Restart (Catch on the fly): Restarts the motor at the estimated speed the motor is already going. nO – Function inactive YES – Function active | nO |
| tHt- | ItH | Motor Thermal Current | varies |

Fault Detection

The AC drive has a comprehensive fault diagnostic system that includes several different alarms and fault messages. Once a fault is detected, the corresponding protective functions will be activated. The following faults are displayed as shown on the AC drive digital keypad display.

Note

Not all faults can be cleared by resetting from the drive keypad. Some faults can only be cleared by cycling power on the drive, and some faults cannot be reset at all.

| Code | Name | Possible Cause | Remedy |
| --- | --- | --- | --- |
| CrF1 | Precharge | Charging relay control fault or charging resistor damaged | Turn the drive off and then back on again Check the connections Check the stability of the main supply Contact your local Schneider Electric representative |
| InFI | Unknown drive rating | The power card is different from the card stored | Contact your local Schneider Electric representative |
| InF2 | Unknown or incompatible power board | The power card is incompatible with the control card | Contact your local Schneider Electric representative |
| InF3 | Internal serial link | Communication interruption between the internal cards | Contact your local Schneider Electric representative |
| InF4 | Invalid industrialization zone | Inconsistent internal data | Contact your local Schneider Electric representative |
| InF9 | Current measurement circuit | Current measurement is not correct due to hardware circuit | Contact your local Schneider Electric representative |
| ---- | Problem of application Firmware | Invalid application firmware update using the Multi-Loader tool | Flash again the application firmware of the product |
| InFb | Internal thermal sensor detected fault | The drive temperature sensor is not operating correctly The drive is in short circuit or open | Contact your local Schneider Electric representative |
| InFE | Internal CPU | Internal microprocessor | Turn the drive off and then back on again Contact your local Schneider Electric representative |
| OCF | Overcurrent | Parameters in the Motor Control menu (drC) are not set properly Inertia or load too high Mechanical locking | Check the parameters Check the size of the motor/drive/load Check the state of the mechanism Connect line chokes Reduce the Switching Frequencies (SFr) Check the ground connection of drive, motor cable, and motor insulation |
| OCF | Motor short circuit | Short-circuit or grounding at the drive output Ground fault during running status Commutation of motors during running status Significant current leakage to ground if several motors are in parallel | Check the cables connecting the drive to the motor, and the motor insulation Connect motor chokes |
| SCF1 | Ground short circuit |  |  |
| SCF4 | IGBT short circuit | Internal power component short circuit detected at power on | Contact your local Schneider Electric representative |
| SOF | Over-speed | Instability or over-speed associated with the inertia of the application | Check the motor Over-speed is 10% more than the maximum frequency (tFr). Adjust this parameter if necessary Add a braking resistor Check the size of the motor/drive/load Check the parameters of the speed loop (gain and stability) |
| tnF | Auto-Tuning | Motor not connected to the drive One motor phase loss Special motor Motor is rotating | Check that the motor/drive are compatible Check that the motor is present during auto-tuning If an output contactor is being used, close it during auto-tuning Check that the motor is completely stopped |
| LFFI | AI current lost fault | Detection if: Analog input AI1 is configured as current AI1 current scaling parameter of 0% is greater than 3mA Analog input current is lower than 2mA | Check the terminal connections |
| ObF | Over-braking | Braking too sudden or driving load | Increase the deceleration time Install a module unit with a braking resistor if necessary Check the line supply voltage to be sure it is under the maximum |
| OHF | Drive overheat | Drive temperature too high | Check the motor load, the drive ventilation, and the ambient temperature. Wait for the drive to cool down before restarting. |
| OLC | Process overload | Process overload | Check the process and the parameters of the drive to be in phase |
| OLF | Motor overload | Triggered by excessive motor current | Check the setting of the motor thermal protection, check the motor load |

| OPF1 | 1 output phase loss | Loss of one phase at drive output | Check the connections from the drive to the motor In case of downstream contactor, check the right connection, cable, and contactor |
| --- | --- | --- | --- |
| OPF2 | 3 output phase loss | Motor not connected Motor power too low, below 6% of the drive nominal current Output contactor open Instantaneous instability in the motor current | Check the connections from the drive to the motor Test on a low power motor or without a motor: In factory settings mode, motor phase loss detection is active Output Phase loss detection OPL = YES to check the drive in a test or maintenance environment, without having to use a motor with the same rating as the drive, deactivate motor phase loss detection Output Phase loss detection OPL = nO Check and optimize the following parameters: IR compensation (law U/F) UFr , Rated motor voltage UnS and Rated motor current nCr and perform an Auto-tuning tUn |
| OSF | Main overvoltage | Line voltage too high Disturbed line supply | Check the line voltage |
| PHF | Input phase loss | Drive incorrectly supplied or a fuse blown Failure of one phase 3-phase ATV12 used on a single-phase line supply Unbalanced load This protection only operates with the drive on load | Check the power connection and the fuses. Use a 3-phase line supply. Disable the fault by setting Input Phase loss detection IPL |
| SCF5 | Load short circuit | Short-circuit at drive output Short circuit detection at the run order or DC injection order if parameter IGBT test Strt is set to YES | Check the cables connecting the drive to the motor, and the motor’s insulation |
| SLF1 | Modbus Communication | Interruption in communication on the Modbus network | Check the connections of communication bus. Check the time-out (Modbus time out ttO parameter Refer to the Modbus user manual |
| SLF2 | SoMove Communication | Communication interruption with SoMove | Check the SoMove connecting cable. Check the time-out |
| SLF3 | HMI Communication | Communication interruption with the external display terminal | Check the terminal connection |

| SPIF | PI Feedback detected fault | PID feedback below lower limit | Check the PID function feedback Check the PI feedback supervision threshold LPI and time delay tPI |
| --- | --- | --- | --- |
| ULF | Process underload fault | Process underload Motor current below the Application Underload threshold LUL parameter during a period set by Application underload time delay ULt parameter to protect the application. | Check the process and the parameters of the drive to be in phase |
| tJF | IGBT overheat | Drive overheated IGBT internal temperature is too high according to ambient temperature and load | Check the size of the load/motor/drive. Reduce the Switching frequency SFr. Wait for the drive to cool before restarting |
| CFF | Incorrect configuration | HMI block replaced by an HMI block configured on a drive with a different rating The current configuration of customer parameters is inconsistent | Return to factory settings or retrieve the backup configuration, if it is valid. If the fault remains after reverting to the factory settings, contact your local Schneider Electric representative |
| CFI | Invalid configuration | Invalid configuration The configuration loaded in the drive via the bus or communication network is inconsistent. The configuration upload has been interrupted or is not fully finished. | Check the configuration loaded previously. Load a compatible configuration |
| CHI2 | Download invalid configuration | Interruption of download operation with Loader or SoMove | Check connection with Loader or SoMove. To reset the default re-start the download operation or restore the factory setting |
| USF | Undervoltage | Line supply too low Transient voltage dip | Check the voltage and the parameters of Undervoltage Phase Loss Menu USb |

Optional Height Detection Sensor

The optional ultra-sonic sensor may be purchased to replace the standard height detection photoelectric sensor.

Ultrasonic Sensing Concept

Ultrasonic sensors emit and receive sound at frequencies above the range of human hearing (above 20 kHz). They sense objects by measuring the time it takes to reflect the ultrasonic sound waves from the object’s surface and back to the receiver, or by detecting an object’s presence when it interrupts the transmission of sound from the emitter to an opposed receiver. Unlike infrared photoelectric sensing, which is based on an object’s opacity or reflectivity to light, ultrasonic sensing depends on object’s density—it’s ability to reflect or block sound. This makes ultrasonic sensing practical for detection of clear or black materials and other objects that are difficult to detect with photoelectric sensors.

Figure 6: Ultrasonic Sensing Concept

Load Compression Testing

Load compression tests were designed to allow you to measure the force of the film against your product. These tests will allow you to fine tune the machine for the most secure products.

- Place a product in the center of the wrap area.

- Attach the film to the product.

- Set the Film Force potentiometer dial to about 50%.

- Initiate a wrapping cycle by pressing the Start button on the operator panel. To test the load compression, allow the machine to complete one full cycle.

- Using the tape measure provided in the optional Highlight Field Test Kit FTK-4000, determine as close as possible the center of one side of the product.

- Attach the scale provided in the Highlight Field Test Kit FTK-4000 kit to the center of the package by pushing the pointed end of the hook all the way through the stretch film. Grasp the other end of the scale, and pull it two inches away from the product.

- Record the reading on the scale and the reference number on the Film Force potentiometer. To increase the load compression, rotate the dial clockwise to a higher reference number, or rotate counter-clockwise to decrease the load compression.

- Remove all the stretch film from the product.

- Repeat the above steps if additional adjustments are needed.

The final setting which best suits your load will remain the same until you change the Film Force setting or stretch level.

Optional Scale Package

The optional scale package allows the user to quickly measure the weight of a package placed on the machine. To operate correctly and efficiently the scale needs to be configured with the correct settings. Below are instructions on how to re-configure the scale and the settings that have been pre-programmed. Re-configuring the scale is not required unless there is a problem with the existing scale or a new scale is added to the machine. Refer to the scale manual for more information.

Note

Changing the scale parameters to values other than the Highlight recommended values may result in poor scale operation.

Navigating the Scale Menu

Step 1: Turn the scale display over so you are looking from above down at the back side of the scale and turn off the scale power.

Step 2: Remove the two small screws holding a small plate on the back of the scale.

Step 3: Looking down at the scale, move the switch under the plate to the right.

Step 4: Turn the scale power back on.

Step 5: Press the “PRINT / >>” button until the desired setting appears on the screen.

Step 6: Press the “ZERO” button to enter the parameter set-up.

Step 7: Press the “PRINT / >>” button until the display reads the correct setting and press the “SET / NET” button.

Step 8: Turn the power back off, move the switch under the plate to the left, and turn the power back on.

Step 9: Replace the screws on the back cover and retighten the scale swivel grips on the side.

Step 10: The scale is now ready to use.

Highlight Recommended Configuration Values

Note

Changing the scale parameters to values other than the Highlight recommended values may result in poor scale operation.

| Name/Code | Description | Highlight Suggested Value |
| --- | --- | --- |
| F1: Graduations | Specifies the number of full-scale graduations. Value should be consistent with legal requirements and environmental limits on the useful system resolution. | 5000 |
| F2: Span Gain | Span Gain is related to A/D integration time. The larger the span gain, the higher the internal resolution, but the slower the update speed. Note that the scale must be re-calibrated whenever this parameter is altered. See Appendix C in the scales manual for more information. | 100 |
| F3: Zero Track Band | Selects the range within which the scale will automatically zero. Note that the scale must be in a standstill to zero the scale. | 3 |
| F4: Zero Range | Selects the range within which the scale may be zeroed. Note that the indicator must be in standstill to zero the scale. | 100 |
| F5: Motion Band | Sets the level at which motion is detected by comparing the present display update with the previous one. If motion is not detected for two seconds or more, scale is in standstill and can process a Print or Zero command. Maximum value varies depending on local regulations | 1 |
| F6: Digital Filter | Averages weight readings to produce higher stability but the slower the indicator’s response time. Choose 8 unless a very fast response is needed. | 8 |
| F7:Overload Limit | Selects the desired formula which determines the point at which the indicator shows overload. All selections are based on the primary unit selected in F8. | 2% |
| F8: Calibration Unit | Selects the primary base unit to be used in the calibration process. Also the default unit for normal operation. 1 = pounds, 2 = kilograms. | 1 |
| F9: Display Divisions | Determines the desired weight increments. Value should be consistent with legal requirements. | 1 |
| F10: Decimal Point | Determines the location of the decimal point. | 0 |
| F16:Zero Calibration | Places the scale in a Zero Calibration routine. See below. | See below. |
| F17: Span Calibration | Places the scale in a Span Calibration routine. See below. | See below. |

Scale Calibrating Procedure

Note

Highlight Industries, Inc. calibrates the scale before shipment using known weights. The values stored in these settings are custom per scale and machine. Do not change these values unless directed to do so by Highlight personnel.

Step 1: Navigate the scale menu to parameter “F 16.”

Step 2: Press the “ZERO” button ONCE. This enters the Zero Calibration Menu. The display will momentarily show “C 0” followed by a value.

Step 3: After making sure that there are no test weights on the machine press the “ZERO” button again. The display will zero.

Step 4: Press the “SET / NET” button to save the zero point value. The display will show “EndC0” momentarily then revert to parameter F16.

Step 5: Navigate to parameter “F 17.”

Step 6: Press the “ZERO” button ONCE. This enters the Span Calibration Menu. The display will momentarily show “C 1” followed by a value with one flashing digit. This value will be zero with the decimal point parameter selected in F10.

Step 7: Place a known weight on the machine. Ensure that the test weight is below the maximum capacity of the scale and above 1% of the maximum capacity of the scale.

Step 8: Key in the weight of the test weight using the buttons on the screen. Press the “TARE / <<” button to select the digit to the left of the current position. Press “PRINT / >>” to select the digit to the right of the current position. Press “UNITS” to increase the value of the digit and press “ZERO” to decrease the value of a digit.

Step 9: Once the weight of the test weight is keyed in exactly, press the “SET / NET” button to save the value. If the calibration was successful the display will read “EndC1” momentarily, and then revert back to “F17”. If “Err0” is displayed the test weight is larger than the full capacity of the scale. If “Err1” is displayed the test weight is below 1% of the full capacity of the scale. If “Err2” is displayed the internal resolution of the scale is not high enough to accept the calibration value

4

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

Operation Instructions

Operator Controls

Operator Panel Button Controls

Figure 7: Operator Panel

Emergency Stop

The “E-STOP” button cuts machine operation and removes power to frequency drives. In the event this button is pressed during the course of operation, it is necessary to pull this button fully out to reset the machine.

Warning!

If the Emergency Stop button is pressed while the turntable is rotating, the turntable will NOT stop immediately, but rather it will decelerate and possibly coast to a stop.

Start

The “Start” button initiates all operations, in automatic or manual modes. When the system is in automatic mode, the button LED stays on until the wrapping cycle is complete. In manual mode, the button LED flashes until the operation is stopped.

Reset

After “Stop” button is pressed, the “Reset” button cancels the wrapping cycle and sends the turntable and film carriage into their respective home positions.

Stop

The “Stop” button pauses all operations in automatic mode. To resume the wrapping cycle, simply press the “Start” button. To clear the cycle, press the “Reset” button.

Film Force

The “Film Force” potentiometer dial determines the amount of film tension applied to the load in a wrapping cycle. Turn clockwise to increase, counter-clockwise to decrease. The best product wrapping and proper dancer bar response is achieved when the dancer bar is set to between half and two thirds of its full extension. This gives the proper force to load setting and allows a good proportion of the spring return travel on the dancer bar to be used when the turntable slows down at the end of cycle.

Carriage/Elevator Speed

The “Carriage/Elevator Speed” potentiometer dial determines the speed of the turntable in both automatic and manual modes. Turn clockwise to increase, counter-clockwise to decrease. Adjusting this will affect the film overlap.

Turntable Speed

The “Turntable Speed” potentiometer dial determines the speed of the turntable in both automatic and manual modes. Turn clockwise to increase, counter-clockwise to decrease. Adjusting this will affect the film overlap. The maximum turntable speed is 12 rotations-per-minute (RPM).

Operator Panel Touch Screen Controls

Below is a short description of the function for each screen. See each screen’s Help Screen for more details about specific operation of the functions on the screen.

Start Screen

The Touchscreen powers up to this screen. Simply press the button to go to other control screens.

Main Screen

The Main Screen provides navigation to all other screens. It also provides user login access to gain access to restricted screens.

Alarm Screens

The Current Alarm Screen displays all alarms that are active. The alarms disappear when the alarm condition is cleared. The Alarm History Screen provides a history of all past and current alarms since the power to the machine was cycled. Current alarms are highlighted green, while past alarms appear red.

Mode Select Screen

The Mode Select Screen allows the operator to switch between the different wrap modes and modes of operation.

Status Screen

The Status Screen displays current system information, and allows an operator with access to restricted screens to reset the daily cycle count.

Manual Screen

The Manual Screen allows an operator to control different portions of the machine manually. Simply press each button to use the features described. The wrap cycle must not be running to use the manual buttons.

Timer Setup Screen

The Timer Setup Screen allows an operator with access to restricted screens to adjust the system timers that determine machine operation.

Counter Screen

The Counter Screen allows an operator with access to restricted screens to adjust the system counters that determine machine operation while in automatic mode.

Film Out Screen

The Film Out Screen describes the procedure for handling a film out condition.

Film Loading

Follow the procedure below to thread the film onto the Film Carriage.

Warning!

Be sure the Emergency Stop button is pressed before threading the film and while the film is being threaded.

- Rotate the handle and open the film carriage.

- Pull six (6) feet of film off the film roll.

- Follow the diagram below and “thread” the 6-foot film tail all the way through the rollers.

- Close the film carriage and rotate the handle in the opposite direction to lock.

- Attach the film securely to the pallet. Tying the end of the film in a knot often helps to secure the film to the pallet.

Figure 8: Film Loading/Threading Diagram

Machine Operating Instructions

Running a Wrap Cycle

- To start a new wrap cycle, first place the product to be wrapped on the turntable, thread the film through the carriage, and attach the film to the product.

- Ensure that the turntable and film carriage are at their home positions.

- Set the desired number of Top and Bottom wraps.

- Select the desired Wrap Mode to be applied to the product.

- Turn the Turntable and Film Carriage selector switches to the Auto position.

- Press the Cycle Start button on the operator panel to initiate the wrap cycle.

Emergency Stop

If there is a need to press the emergency stop button, all motive power will be removed. The turntable will attempt to stop as fast as possible, but may coast to a stop. Pull the E-Stop button out to restore power, and then start a new cycle following the Running a Wrap Cycle steps.

Film Out

A film out condition is detected when the dancer bar is relaxed and the dancer bar switch is off for a period of three seconds. Once a film out is detected, the turntable and the film carriage will return to their home positions and stop. An operator is now able to reload the film into the carriage. Simply pressing the start button again will cause the wrap sequence to re-start.

Applying Reinforcement Wraps

Automatic operation can be paused in order to apply reinforcement wraps to an additional top sheet or corner boards on the product. Follow the procedure below.

- Press the “Start” button as normal to initiate cycle.

- As the carriage travels up, switch the “Turntable” selector from Auto to Manual. Both the turntable and the film carriage will pause.

- Apply the top sheet or corner boards to the product.

- Press the “Start” button to resume cycle. Leave the “Turntable” selector switch in Manual position. The turntable will now rotate in Manual mode.

- Once the reinforcement wraps have been applied, switch the “Turntable” selector switch from Manual to Auto. The turntable will pause.

- Press the “Start” button again to complete the automatic operation.

If the “Turntable” selector is switched from Auto to Manual while the carriage is traveling down, the carriage will travel back up and apply the top wraps before completing the wrap cycle. This to ensure the top sheet applied during the manual operation is properly wrapped into the product.

Film Cutting

Automatic Film Cutting

The automatic film cut feature is always enabled in the automatic mode. After the last wrap of the cycle the turntable will return to home and stop, held in place by the table interlock. The wiper arm will then extend towards the package and the hot wire will heat and cut the film as the wiper rotates against the package. When it is finished cutting and wiping down the film tail, the wiper arm will remain extended till the package is removed from the turntable.

5

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

Maintenance

Preventative Maintenance

As with all machinery, proper attention and maintenance is the key to long component life, maximum performance, and safe operation.  By spending a few minutes reading and following these preventive measures, you should reduce the downtime and prolong the life of your system.

It is important to understand that these maintenance schedules are minimum recommendations.  Highlight Industries, Inc. cannot possibly know, evaluate, or advise the various trades in all schedules of periodic maintenance. Accordingly, anyone who maintains or services a stretch wrap machine must first satisfy himself/herself as to the schedules of preventive maintenance based on cycling operation and environmental locations.

Warning!

All maintenance operations require the equipment to be powered down and locked out for personnel safety.

Lock-out/ Tag-out Procedures

Be sure that anyone performing any type of maintenance on this equipment is familiar with and is adhering to the lock-out/tag-out procedures set forth by the General OSHA or the State OSHA guidelines.

Visual Checks

Visual checks should be conducted at least once per month:

- Keep the machine and surrounding area as clean as possible, especially near moving components.

- Check for loose hardware, especially set screws located in: sprocket hubs, bearing hubs, and flanges.

- Check for loose cotter pins.

- Check for oil leaks around the speed reducers.

- Check for dry seals at the bearings.

- Check for chain wear and proper tension on the power roller stretch sprockets.  The correct amount of chain tension can be checked by pulling the chain taut and having 3/8” slack.

- Check for fraying lift belts on the film carriage lift system.

- Check for loose electrical connections and for frayed cords and cables. Replace immediately any damaged cords and cables.

Turntable Belt Adjustment

Refer to figure below to adjust the turntable belt. First, loosen the four motor flange (M10) screws. Turn the (M10) bolt on the adjuster tab until the belt is tensioned. Retighten the four motor flange screws.

Figure 9: Turntable Belt Adjustment

Film Carriage Lift Chain Adjustment

Refer to figure below to adjust the film carriage lift chain. First, loosen nut (M12) on the adjustment bracket. Turn the bottom bolt until desired tension is achieved. Retighten nut (M12). Note that the driving chain and adjustment bracket should be parallel with the moveable pulley base.

Figure 10: Film Carriage Lift Chain Adjustment

Sprockets and Chains

All sprockets should be inspected for wear, and chains should be checked for proper tension and lubrication on a periodic basis. Failure to do so will lead to premature sprocket failure. Any general-purpose chain lube should be sufficient for lubrication. Replace chain guards when preventative maintenance is complete.

Maintenance Schedule

| Part | Schedule | Service With |
| --- | --- | --- |
| Turntable Reducer | Sealed, lubricated with premium lubricant. No maintenance required. | N/A |
| Film Carriage Reducer | Sealed, lubricated with premium lubricant. No maintenance required. | N/A |
| Film Delivery Reducer | Sealed, lubricated with premium lubricant. No maintenance required. | N/A |
| All pivot bearings | Initially first 1,000 cycles; every 10,000 cycles thereafter. | Mobil EP-1 grease |

Note

For additional maintenance information about specific components on the machine, refer to the components operation manuals shipped inside the main enclosure.

6

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

Trouble-shooting

Troubleshooting Guide

Warning!

Make sure that only qualified personnel will perform inspection, troubleshooting, and part replacement.

High Voltage!

Disconnect all power including external control power that may be present before servicing the frequency drive controllers. Wait three (3) minutes for the DC bus capacitors to discharge. The frequency drive controller display and/or LED’s are not accurate indicators of the absence of DC bus voltage.

Before You Start

The diagrams in this section will guide you in identifying typical problems while operating the Predator Platinum Turntable Stretch Wrapper, and provide you with corresponding solution(s). Problems are divided in reference to the machine functions: power, turntable, film carriage, and film delivery.

If further assistance is required, contact the distributor from whom you have purchased the equipment, or call the number listed on the bottom page of this manual. To receive quick and proper technical support, please be prepared to provide the following information:

- Machine serial number

- Date of purchase

- Symptoms of any problems

General Troubleshooting Practices

- Always adhere to the General OSHA or the State OSHA guidelines.

- When working with machine wiring, take precautions to prevent contact with live wires.

- Ensure that all wiring is securely fastened and that all terminals are tightened down properly.

- Have a multi-meter nearby to be able to check for voltages and continuity on different portions of the machine circuitry.

- Use the schematics provided in this manual to trace wiring and find components on the sub panel.

Power Problems

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The machine does not power up. | The Emergency Stop button is pressed. | Pull the Emergency Stop button fully out, then release to restore power. |
|  | The film carriage foot safety switch on the bottom of the carriage is tripped. | Clear any obstructions under the film carriage. Ensure the pan can move freely up and down. |
|  | The control box door is open. | Close the control box door. |
|  | The film carriage door is open. | Close the film carriage door. |
|  | The machine is not plugged in. | Plug the machine into a 120VAC, 15A outlet. |
|  | The Main Disconnect is turned off. | Turn the Main Disconnect on. |
|  | The main circuit breaker is tripped or off. | Turn the breaker back on, or replace if necessary. |
|  | The 24VDC supply is off or malfunctioned. | Ensure the circuit breakers before and after the DC power supply are on. |
|  |  | Use a voltmeter to check that the power supply is receiving 120VAC and supplying 24VDC. Replace if necessary. |
|  | The main contactor has malfunctioned. | Check wiring to the contactor, or replace if necessary. |
| The display on a Frequency Drive is not on. | The machine is not powered up. | See above solutions. |
|  | The drive has malfunctioned. | Check wiring to the Frequency Drive, or replace if necessary. |

Turntable Problems

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The turntable does not rotate manually. | The Frequency Drive is not on (the drive display is off). | See the Power Problems section. |
|  | The turntable speed is not set high enough. | Adjust Turntable Speed potentiometer towards 100%. |
|  | The turntable speed potentiometer has malfunctioned. | Use a multi-meter to check is the potentiometer is working correctly. Replace as necessary. |
|  | The Frequency Drive is faulted. | Record the fault code on the drive display and refer to the Frequency Drive Adjustments section of this manual or the drive manufacturer’s manual. |
|  | The turntable is mechanically restricted. | Check the condition of the motor, chain, and rollers under the turntable. Replace as necessary. |
|  | The turntable motor is not wired correctly. | Check connections between the Frequency drive and the motor. Ensure the motor is wired for the correct voltage. Replace the motor as necessary. |
|  | The PLC has malfunctioned | Check wiring to the PLC and replace as necessary. |
|  | The Frequency Drive has malfunctioned. | Check wiring to the Frequency Drive and replace as necessary. |
|  | The parameters in the Frequency Drive are not set properly. | Refer to the Electrical Schematics in the Technical References section of this manual for Highlight Industries, Inc. factory drive settings. |

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The table does not rotate during the wrap cycle. | The Frequency Drive is not on (the drive display is off). | See the Power Problems section. |
|  | The Frequency Drive is faulted. | Record the fault code on the drive display and refer to the Frequency Drive Adjustments section of this manual or the drive manufacturer’s manual. |
|  | The turntable is mechanically restricted. | Check the condition of the motor, chain, and rollers under the turntable. Replace as necessary. |
|  | The turntable motor is not wired correctly. | Check connections between the Frequency drive and the motor. Ensure the motor is wired for the correct voltage. Replace the motor as necessary. |
|  | The turntable speed is not set high enough. | Adjust Turntable Speed potentiometer towards 100%. |
|  | The Cycle Start button has malfunctioned. | Check wiring to the button and replace as necessary. |
|  | The PLC has malfunctioned | Check wiring to the PLC and replace as necessary. |
|  | The Frequency Drive has malfunctioned. | Check wiring to the Frequency Drive and replace as necessary. |
|  | The parameters in the Frequency Drive are not set properly. | Refer to the Electrical Schematics in the Technical References section of this manual for Highlight Industries, Inc. factory drive settings. |
| The turntable does not stop at home. | The Turntable Deceleration Delay is set too long. | Decrease the Turntable Deceleration Delay. See the Pre-Operation Adjustment section of this manual for instructions. |
|  | The Turntable Home proximity switch is malfunctioning. | Check the wiring to the proximity switch and that it is adjusted properly (only 8mm sensing range). Replace as necessary. |
|  | The Frequency Drive deceleration parameter (DEC) is set too low or too high. | If the setting is too high, it may pass the home position before stopping. Refer to the Electrical Schematics in the Technical References section of this manual for Highlight Industries, Inc. factory settings. |

Film Carriage Problems

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The Film Carriage does not Raise or Lower manually or in the wrap cycle. | The Carriage speed is set too low. | Adjust the carriage speed potentiometer towards 100%. |
|  | The carriage speed potentiometer has malfunctioned. | Use a multi-meter to check is the potentiometer is working correctly. Replace as necessary. |
|  | The Film Carriage Raised/Lowered limit switch is malfunctioning. | Ensure that the carriage limit switch is clear of any obstruction and moves smoothly. Check wiring to the limit switch and replace as necessary. |
|  | The Frequency Drive is not on (the drive display is off). | See the Power Problems section. |
|  | The Frequency Drive is faulted. | Record the fault code on the drive display and refer to the Frequency Drive Adjustments section of this manual or the drive manufacturer’s manual. |
|  | The Carriage is mechanically restricted. | Check the condition of the motor and belts. Replace as necessary. |
|  | The Carriage motor is not wired correctly. | Check connections between the Frequency drive and the motor. Ensure the motor is wired for the correct voltage. Replace the motor as necessary. |
|  | The PLC has malfunctioned | Check wiring to the PLC and replace as necessary. |
|  | The Frequency Drive has malfunctioned. | Check wiring to the Frequency Drive and replace as necessary. |
|  | The parameters in the Frequency Drive are not set properly. | Refer to the Electrical Schematics in the Technical References section of this manual for Highlight Industries, Inc. factory drive settings. |
|  | The Turntable Home proximity switch is malfunctioning. | Check the wiring to the proximity switch and that it is adjusted properly (only 8mm sensing range). Replace as necessary. |

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The Film Carriage rises some, but does not rise to the top of the package. | The Product Height Detection photo eye is positioned too high. | Slide the Product Height Detection photo eye lower. |
|  | The Product Height Detection photo eye does not see the load. | Black or clear loads may require an optional ultrasonic sensor instead of the standard diffuse sensor. |
|  |  | Check wiring to the sensor. |
|  |  | Replace the sensor as necessary. |
|  | The Package Height Detection Delay is set too low. The sensor may not see the load at all times. Use this setting to filter out these dead spots. | Increase the package height detection delay using the Pot 0 (right pot) on the PLC itself. |
|  | The Product Height Detection photo eye is not adjusted properly. | Adjust position or sensitivity of the sensor (see the Photo Sensor Adjustments and/or Pre-Operation Adjustments section). |
| The Film Carriage rises too far above the package. | The Product Height Detection photo eye is positioned too low. | Slide the Product Height Detection photo eye higher. |
|  | The Product Height Detection photo eye is not adjusted properly and always sees a ’package’. | Adjust the sensitivity of the sensor (see the Photo Sensor Adjustments and/or Pre-Operation Adjustments section). |
|  | The Package Height Detection Delay is set too high. | Decrease the package height detection delay using the Pot 0 (right pot) on the PLC itself. |

Film Delivery Problems

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The Film Delivery motor does not run manually or during a wrap cycle. | The Film Carriage Door is open. | Ensure door is closed and that the door limit switch is operating correctly. |
|  | The Film Force potentiometer is set too high. | Turn the potentiometer counter-clockwise (to a lower number) to decrease the force and increase film delivery speed. |
|  | The film force potentiometer has malfunctioned. | Use a multi-meter to check is the potentiometer is working correctly. Replace as necessary. |
|  | The Frequency Drive is not on (the drive display is off). | See the Power Problems section. |
|  | The Frequency Drive is faulted. | Record the fault code on the drive display and refer to the Frequency Drive Adjustments section of this manual or the drive manufacturer’s manual. |
|  | The motor is mechanically restricted. | Check the condition of the motor, chain, and rollers/mandrels on the Film Carriage. Replace as necessary. |
|  | The PLC has malfunctioned. | Check wiring to the PLC and replace as necessary. |
|  | The Frequency Drive has malfunctioned. | Check wiring to the Frequency Drive and replace as necessary. |
|  | The parameters in the Frequency Drive are not set properly. | Refer to the Electrical Schematics in the Technical References section of this manual for Highlight Industries, Inc. factory drive settings. |
|  | The Dancer Bar limit switch does not get tripped when the Dancer Bar is extended. | Adjust the switch so that it trips when the Dancer bar is pulled. |
|  |  | Check wiring to the switch and replace as necessary. |
| The film breaks at the start of the wrap cycle. | The film is not threaded properly. | Use the Film Loading Diagram located on the carriage to thread the film correctly. |
|  | The film Quality is too low. | Use films that are free of holes or snags. |
|  | The Pre-Stretch level is set too high. | Decrease the film Pre-Stretch level following the Pre-Stetch Percentage Change instructions. |

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The Film Delivery motor does not run during a wrap cycle. | The Film Force Potentiometer is set too high. | Turn the potentiometer counter-clockwise (to a lower number) to decrease the force and increase film delivery speed. |
| The film breaks during the wrap cycle. | The Film Force Potentiometer is set too high. | Turn the potentiometer counter-clockwise (to a lower number) to decrease the force and increase film delivery speed. |
|  | The Film Force Potentiometer is malfunctioning. | Check wiring to the Film Force Potentiometer and replace as necessary. |
|  | The film is not threaded properly. | Use the Film Loading Diagram located on the carriage to thread the film correctly. |
|  | The film Quality is too low. | Use films that are free of holes or snags. |
|  | The Pre-Stretch level is set too high. | Decrease the film Pre-Stretch level following the Pre-Stetch Percentage Change instructions. |
| The film is not being stretched during the wrap cycle. | The Pre-Stretch level is set too low. | Increase the film Pre-Stretch level following the Pre-Stetch Percentage Change instructions. |
|  | The film is not threaded properly. | Use the Film Loading Diagram located on the carriage to thread the film correctly. |
|  | The film is slipping on the stretch rollers | Ensure the film cling will be on the package side as the film is wrapped around the package. |
|  |  | Ensure the main film mandrel provides drag on the film. Tighten the mandrel if it is too loose. |
| The film is being stretched too much during the wrap cycle. | The Pre-Stretch level is set too high. | Increase the film Pre-Stretch level following the Pre-Stetch Percentage Change instructions. |
|  | The film is not threaded properly. | Use the Film Loading Diagram located on the carriage to thread the film correctly. |
|  | The Film Force Potentiometer is set too high. | Turn the potentiometer counter-clockwise (to a lower number) to decrease the force and increase film delivery speed. |

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| The Film Delivery Motor does not shut off. | The dancer bar limit switch is not adjusted properly. | Adjust the switch so that it trips when the Dancer bar is pulled. |
|  |  | Check wiring to the switch and replace as necessary. |
|  | The PLC has malfunctioned. | Replace the PLC. |

Film Cut Problems

| Problem | Possible Cause | Possible Solution |
| --- | --- | --- |
| Wiper arm does not extend when operated manually. | The compressed air supply is not attached. | Attach the compressed air supply. |
|  | The PLC has malfunctioned. | Check the PLC output indicator light for the wiper, and check the wiring to the PLC. Replace if necessary. |
|  | The wiper arm proximity switches are obstructed or malfunctioning. | Remove obstruction and/or clean proximity switch. Check power to the switch and replace if necessary. |
|  | The wiper arm valve on the tower is not letting air through. | Turn the handle on the valve to let more air pass, or replace if it is not working properly. |
| The wiper itself does not move when the “Cut Film” button is pressed. | The compressed air supply is not attached. | Attach the compressed air supply. |
|  | The PLC has malfunctioned. | Check the PLC output indicator light for the wiper, and check the wiring to the PLC. Replace if necessary. |
|  | The wiper proximity switches are obstructed or malfunctioning. | Remove obstruction and/or clean proximity switch. Check power to the switch and replace if necessary. |
|  | The wiper valve on the tower is not letting air through. | Turn the handle on the valve to let more air pass, or replace if it is not working properly. |
| The hot wire does not heat up when the “Cut Film” button is pressed. | The PLC has malfunctioned. | Check the PLC output indicator light for the wiper, and check the wiring to the PLC. Replace if necessary. |
|  | The hot wire relay has malfunctioned. | Use a voltmeter to make sure that the correct power is being supplied to the relay. Refer to the power problems section. |
|  | The hot wire is not wired correctly. | Inspect the wiring, tighten connections, and replace if necessary. |

7

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

Technical References

Recommended Spare Parts

The table below provides the recommended spare parts list for the Predator Platinum Turntable Stretch Wrapper.

| Part Number | Description | Quantity |
| --- | --- | --- |
| 301495 | DRIVE BELT, 148” | 1 |
| 403556 | T.T. HOME & STRETCH % PROX. | 1 |
| 700060 | T.T. CAM FOLLOWER ASS’Y | 6 |
| 400637 | CARRIAGE DOOR LIMIT SWITCH | 1 |
| 400671 | CARRIAGE SAFETY LIMIT SWITCH | 1 |
| 400639 | CARR. UPPER/LOWER LIMIT SWITCH | 1 |
| 400643 | LOAD HT. DETECTION PHOTO EYE | 1 |
| 400644 | CONTROL BOX SAFETY SWITCH | 1 |
| 500080 | CONTROL BOX SAFETY KEY | 1 |
| 400618 | SELECTOR SWITCH, 2 POSITION | 1 |
| 400619 | SELECTOR SWITCH, 3 POSITION | 1 |
| 400620 | POTENTIOMETER KNOB | 1 |
| 400649 | POTENTIOMETER, 5K | 1 |
| 400613 | E. STOP SWITCH | 1 |
| 400621 | MAIN DISCONNECT SWITCH | 1 |
| 403172 | CONTACTOR | 1 |
| 408806 | DELTA DRIVE INVERTER 120VAC | 1 |
| 408093 | NI-CHROME WIRE, 21 GA. (0.0285dia, 0.8310 ohm/ft) | 30’ |
| 301559 | GEARMOTOR, TURNTABLE DRIVE | 1 |
| 300774 | GEARMOTOR, CARRIAGE LIFT | 1 |
| 301358 | GEARMOTOR, PRESTRETCH, SV-A10 | 1 |
| 304086 | SPRING, DANCER BAR | 1 |
| 301564 | CYLINDER, JAW PIVOT | 1 |
| 306005 | CYLINDER, WIPER PIVOT | 1 |
| 304962 | CYLINDER, TURNTABLE LOCK | 1 |
| 300897 | SOLENOID VALVE, SGL SOL, 24 VDC | 1 |
| 303689 | ROTARY FITTING FOR TURNTABLE | 1 |

Electrical Drawings

Electrical Schematics

This table represents the Electrical Schematics Page 9

Electrical Sub Panel Drawing

Electrical Sensor Layout

Electrical Parts List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

Parts available in inventory are highlighted. Non-highlighted parts may have longer lead times.

| NO. | Part Number | Description | Quantity |
| --- | --- | --- | --- |
| 1 | 408803 | TOUCH SCREEN F940GOT-LWD | 1 |
| 2 | 400609 | AUTO RUN GREEN LAMP | 1 |
| 3 | 400610 | AUTO RUN GREEN LAMP COVER | 1 |
| 4 | 400611 | INDICATOR LIGHT DL1-CE024 | 1 |
| 5 | 400615 | KNOB CONTACTOR ZB2-BZ101C | 2 |
| 6 | 408804 | BUTTON – WHITE | 1 |
| 7 | 408805 | BUTTON – RED | 1 |
| 8 | 401371 | KNOB RN-99F | 3 |
| 9 | 400649 | VARIABLE RESISTOR 5K | 3 |
| 10 | 400613 | EMERGENCY STOP BOTTON | 1 |
| 11 | 400616 | CONTATOR ZB2-BZ102C | 1 |
| 12 | 400621 | MAIN SWITCH | 1 |
| 13 | 408463 | ATV12 115V 1ph IN 230 VAC 3PH OUT 1hp | 3 |
| 14 | 408807 | TRANSFORMER PT-22-C | 1 |
| 15 | 403172 | CONTACTOR | 2 |
| 16 | 403561 | NON-FUSE SWITCH C60A2PC16A | 11 |
| 17 | 400658 | CIRCUIT BOARD | 1 |
| 18 | 408809 | PLC, AXON-24MR-ES | 1 |
| 19 | 408810 | PLC, I/O MODULE, AXON-9EYR | 1 |
| 20 | 408811 | TRANSFORMER PT-27W | 1 |
| 21 | 408812 | TERMINAL TBC-10N30P | 1 |
| 22 | 403174 | POWER SUPPLY S-35-24 (SUB 403133) | 2 |
| 23 | 403565 | CONNECTOR | 1 |
| 24 | 400630 | RELAY LY2, DC24V | 1 |
| 25 | 400638 | RELAY BASE, LY2, PTF-08A | 1 |
| 26 | 400607 | TERMINAL TB6P | 1 |
| 27 | 408815 | DOIDE | 1 |
| 28 | 403169 | FUSE 10, GL | 1 |
| 28 | 403171 | FUSE SEAT | 1 |
| 29 | 403566 | PC BOARD | 1 |
| 30 | 400644 | SAFETY SWITCH XCSPA791 | 1 |
| 31 | 403556 | PROX. SWITCH PM12-04N | 2 |
| 32 | 400643 | PHOTOEYE SENSOR A3R-2MX | 1 |
| 33 | 400639 | LIMIT SWITCH TZ-8108 | 2 |
| NO. | Part Number | Description | Quantity |
| 34 | 400637 | LIMIT SWITCH TZ-7110 | 3 |
| 37 | 408817 | NON-FUSE SWITCH C60NPC2A | 1 |
| 38 | 400646 | RESISTOR 2.2K OHM 1/2W | 1 |
| 39 | 400647 | RESISTOR 2.7K OHM 1/2W | 1 |
| 40 | 404422 | RESISTOR, 3.9K OHM, 1 WATT, 5% | 1 |
| 41 | 408421 | DIODE, 1N4002, GENERAL PURPOSE, 100V | 1 |
| 42 | 400671 | MICRO SWITCH--LEVER ARM | 1 |
| 43 | 400673 | MICRO SWITCH BASE | 1 |

Mechanical Drawings

Turntable Frame Assembly

Turntable Frame Parts List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

Parts available in inventory are highlighted. Non-highlighted parts may have longer lead times.

| NO. | Part Number | Description | Quantity |
| --- | --- | --- | --- |
| 1 | 206848 | FHCS - M10 X 20L | 4 |
| 2 | 600189 | TURNTABLE 1.8M DIA. | 1 |
| 3 | 305996 | BELT BX-145(LI) | 1 |
| 4 | 303685 | PULLEY | 1 |
| 5 | 500779 | BELT PULLEY SEAT RING | 1 |
| 7 | 304544 | BEARING RETENTION PLATE | 1 |
| 8 | 304545 | BEARING 5302ZZ | 1 |
| 9 | 303688 | BELT PULLEY BEARING SEAT | 1 |
| 10 | 200078 | SHCS - M6 x 160 | 4 |
| 11 | 500461 | SENSOR SEAT (PROX BRKT) | 1 |
| 12 | 404579 | PROXIMITY SENSOR (PM12- 04N-3M) | 1 |
| 13 | 500462.2 | SENSOR PLATE (PROX TRIPPER) | 1 |
| A | 700060 | CAM FOLLOWER ASSEMBLY | 18 |
| 14 | 300009 | RING STW-17 | 72 |
| 15 | 500009 | SUPPORTING PLASTIC WHEEL SHAFT | 18 |
| 16 | 500010 | SUPPORTING PLASTIC WHEEL | 18 |
| 17 | 305300 | BEARING 6203ZZ | 36 |
| B | 700601 | BELT RETURN ROLLER ASSEMBLY | 1 |
| 18 | 300009 | RING STW-17 | 1 |
| 19 | 500370 | BELT PULLEY BEARING SEAT | 1 |
| 20 | 305998 | BEARING 6203ZZ | 2 |
| 21 | 500371 | BELT PULLEY BEARING SHAFT | 1 |
| 22 | 200628 | HHCS - M10 X 60L | 1 |
| 23 | 200093 | HHCS - SCREW M10 X 25L | 4 |
| 24 | 301559 | GEAR REDUCER MOTOR | 1 |
| 25 | 600190 | MOTOR BOX | 1 |
| 26 | 500780 | MOTOR BOX COVER | 1 |
| 27 | 200154 | PAN HEAD SCREW M4 X 6L | 4 |
| 28 | 500464 | MOTOR BELT PULLEY | 1 |
| 29 | 600089 | FIXED NUT WELDMENT | 2 |
| 30 | 600191 | TURNTABLE BASE | 1 |
| 31 | 500781 | FRAME COVER | 1 |
| 32 | 200154 | PAN HEAD SCREW M4 X 6L | 4 |
| 33 | 200630 | HHCS - M12 X 35L | 2 |
| 34 | 200140 | M12 HEX NUT | 2 |
| NO. | Part Number | Description | Quantity |
| 35 | 504836 | COVER | 1 |
| 36 | 504837 | GUIDE PLATE | 1 |
| 37 | 504838 | GUIDE PLATE | 1 |
| 38 | 504860 | LIMIT FRAME BASE | 1 |
| 39 | 504861 | LOCKING BASE | 1 |
| 40 | 504862 | WHEEL | 1 |
| 41 | 504863 | TURNING BASE | 1 |
| 42 | 301991 | BUSHING ALFF-1812 | 1 |
| 43 | 504867 | SHAFT | 1 |
| 44 | 200095 | SCREW M10x70L | 1 |
| 45 | 305990 | CBB CYLINDER BASE | 1 |
| 46 | 305991 | PIN (CB TYPE 40) | 1 |
| 47 | 304962 | ISO CYLINDER MCQV-11-40-65M | 1 |
|  | 305993 | CYLINDER SWITCH BASE CQV CB-B40 | 1 |
| 48 | 305994 | Y CONNECTOR∮40 | 1 |
| 49 | 305995 | Y PIN | 1 |
| 50 | 504864 | BRAKE COVER | 1 |
| 51 | 504865 | SPACER RING | 2 |
| 52 | 504866 | FIXED BLOCK | 2 |

Film Jaws and Wiper Arm Assembly

Film Jaws and Wiper Arm Parts List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

| NO. | Part Number | Description | Quantity |
| --- | --- | --- | --- |
| 1 | 600338 | WIPER ARM | 1 |
| 2 | 504845 | UPPER BRACKET COVER, WIPER ARM | 1 |
| 3 | 504846 | UPPER BRACKET, WIPER ARM | 1 |
| 4 | 500800 | RUB STRIP | 1 |
| 5 | 306000 | INSULATOR RING | 4 |
| 6 | 306001 | EYE BOLT | 1 |
| 7 | 306002 | SPRING | 1 |
| 8 | 504850 | HOLDER SHAFT | 2 |
| 9 | 504851 | UPPER WIRE MOUNT | 1 |
| 10 | 504852 | WIPER ARM PLATE | 1 |
| 11 | 504853 | SHAFT | 1 |
| 12 | 504854 | CYLINDER SEAT | 1 |
| 13 | 408093 | HEATING WIRE | 1 |
| 14 | 306004 | FIXEDRING | 4 |
| 15 | 306005 301881 | CYLINDER MCMA-11-32*250A ROD END 81060005 | 1 1 |
| 16 | 306007 | RING | 1 |
| 17 | 306008 | LOWER WIRE MOUNT | 1 |
| 18 | 200654 | SCREW | 2 |
| 19 | 602379.2 | BEARING BLOCK – REF 702505 | 1 |
| 20 | 504855 | FIXED SEAT | 1 |
| 21 | 204402 | PIN | 2 |
| 22 | 602402 | WIPER ARM | 1 |
| 23 | 504856 | WIPER BELT | 1 |
| 24 | 500793 | WIPER BELT REINFORCEMENT STRIP | 1 |
| 25 | 504857 | CYLINDER COVER | 1 |
| 26 | 302027 | BEARING – 25mm | 2 |
| 27 | 504858 | CLAMP FIXED SEAT | 1 |
| 28 | 500782 | SPACER | 2 |
| NO. | Part Number | Description | Quantity |
| 29 | 301564 303857 | CYLINDER MCMA-15-16*75 ROD END 81060005 | 2 2 |
| 30 | 500802.2 | JAW HALF | 1 |
| 31 | 200094 | SCREW M10*50L | 2 |
| 32 | 500803 | FILM JAW BUSHING | 2 |
| 33 | 700662 | JAW HALF | 1 |
| 34 | 500803 | FILM JAW BUSHING | 2 |
| 35 | 500805 | SPACER | 2 |
| 38 | 200090 | SCREW M10*25L | 4 |
| 39 | 504859 | POSITION BLOCK | 1 |
| NS | 303689 | ROTARY AIR FITTING | 1 |
| NS | 304302 | 90 DEGREE AIR FITTING | 4 |

Tower Assembly

Tower Parts List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

Parts available in inventory are highlighted. Non-highlighted parts may have longer lead times.

| No. | Sub No. | Part Number | Description | Quantity |
| --- | --- | --- | --- | --- |
| 1 |  | 600091 | TOWER COVER WELDMENT | 1 |
| 2 |  | 200090 | SHCS, M10 x 25L | 4 |
| 3 |  | 300774 | GEARMOTOR, CARRIAGE LIFT | 1 |
| 4 |  | 300775 | SPROCKET, DRIVEN | 1 |
| 5 |  | 300776 | BRACKET, GEARMOTOR SUPPORT | 1 |
| 6 |  | 300020 | BEARING, 6202-NR | 1 |
| 7 |  | 200631 | SHCS, M5 x 8L | 4 |
| 8 |  | 500466 | BRACKET, LIMIT TRIP | 2 |
| 9 |  | 600092 | TOWER WELDMENT, 80” | 1 |
| 9 |  | 500483 | TOWER WELDMENT – 110” | 1 |
| 10 |  | 500467 | BRACKET, E-CHAIN MOUNT | 1 |
| 11 |  | 300777 | E-CHAIN – 80” TOWER | 1 |
| 11 |  | 500484 | E-CHAIN – 110” TOWER | 1 |
| 12 |  | 500468 | COVER PLATE, 80” TOWER | 1 |
| 12 |  | 500487 | COVER PLATE, 110” TOWER | 1 |
| 13 |  | 200630 | HHCS, M12 x 35L | 2 |
| 14 |  | 200140 | NUT M12 | 2 |
| 15 |  | 200090 | SHCS, M10 x 25L | 6 |
| 16 |  | 200632 | THREADED ROD, M10 x 60L | 2 |
| 17 |  | 500469 | SHAFT, IDLER SPROCKET | 1 |
| 18 |  | 300778 | SPROCKET, IDLER | 1 |
| 19 |  | 300017 | BEARING 6002ZZ | 1 |
| 20 |  | 300008 | SNAP RING, 15mm EXTERNAL | 2 |
| 21 |  | 200084 | SHCS, M8 x 20L | 1 |
| 22 |  | 300029 | CHAIN – 80” TOWER | 1 |
| 22 |  | 500488 | CHAIN – 110” TOWER | 1 |
| 23 |  | 700063 | CHAIN ATTACHMENT ASSEMBLY |  |
|  | W |  | CHAIN TENSION SHAFT |  |
|  | X |  | WASHER, M12 |  |
|  | Y |  | CHAIN ADJUST SEAT |  |
|  | Z |  | NUT M12 |  |
| 27 |  | 500470 | BRACKET, CARRIAGE LIFT | 1 |
| 28 |  | 600093 | CARRIAGE TROLLEY WELDMENT | 1 |
| 29 |  | 500471 | GUIDE WHEEL SHAFT | 3 |
| 30 |  | 500472 | SPACER, INNER | 6 |
| 31 |  | 500473 | GUIDE WHEEL | 6 |
| 32 |  | 305300 | BEARING, 6203 | 6 |
| 33 |  | 500474 | SPACER, OUTER | 6 |
| 34 |  | 200078 | SHCS, M6 x 16L | 6 |
| 35 |  | 500475 | BRACKET, LOWER IDLER PROCKET | 1 |
| 36 |  | 200633 | SHCS, M6 x 10L | 4 |

Film Carriage/Elevator Assembly

Film Carriage/Elevator Parts List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

Parts available in inventory are highlighted. Non-highlighted parts may have longer lead times.

| No. | Sub No. | Part Number | Description | Quantity |
| --- | --- | --- | --- | --- |
| 1 |  | 600179 | STRETCH KNOB COVER | 1 |
| 2 |  | 200636 | WING NUT, M5 x 12L | 2 |
| 3 |  | 200766 | MACHINE SCREW, M4 x 50L | 4 |
| 4 |  | 500661 | STRETCH KNOB HALF | 2 |
| 5 |  | 500662 | GEAR PULL ADAPTER | 1 |
| 6 |  | 500663 | GEAR POSITIONING SHAFT | 1 |
| 7 |  | 301346 | SLIP GEAR, 47T/44T, 200% / 250% | 1 |
| 8 |  | 301365 | SPRING | 2 |
| 9 |  | 500684 | SAFETY BUTTON | 1 |
| 10 |  | 301345 | FIXED GEAR 41T, 200% / 250% | 1 |
| 11 |  | 301344 | FIXED GEAR 44T, 200% / 250% | 1 |
| 12 |  | 300807 | BEARING, 6003ZZ | 2 |
| 13 |  | 500685 | FIXED GEAR SHAFT | 1 |
| 14 |  | 500686 | BEARING SEAT | 1 |
| 15 |  | 200633 | SHCS, M6 x 10L | 3 |
| 16 |  | 600180 | CARRIAGE TOP COVER | 1 |
| 17 |  | 500768 | CARRIAGE COVER BRACKET | 3 |
| 18 |  | 700200 | SPRING KIT ADDED TO TOP | 1 |
| 19 |  | 500673 | SPRING SEAT | 2 |
| 20 |  | 500019 | SPROCKET, 17T | 1 |
| 21 |  | 300846 | CHAIN, inc. MASTER | 1 |
| 22 |  | 204833 | SHCS, M8 x 30L | 4 |
| 27 |  | 500769 | CARRIAGE TOP PAN | 1 |
| 28 |  | 301358 | GEARMOTOR, SV-A10 | 1 |
| 29 |  | 200078 | SHCS, M6 x 16L | 2 |
| 30 |  | 500669 | LIMIT SWITCH BRACE | 1 |
| 31 |  | 500770 | LIMIT SWITCH MNT BRACKET | 1 |
| 32 |  | 400637 | LIMIT SWITCH, TZ-7110 | 1 |
| 33 |  | 200106 | MACHINE SCREW, M4 x 35 | 2 |
| 34 |  | 301343 | GEAR, DRIVE, 19T, 200% / 250% | 1 |
| 35 |  | 301359 | SPROCKET, 12T | 1 |
| 36 |  | 500670 | PROX MOUNT BRACKET | 1 |
| 37 |  | 403556 | PROXIMITY SENSOR, PM12-04N | 1 |
| 38 |  | 700074 | DANCER STOP ASSEMBLY | 2 |
| No. | Sub No. | Part Number | Description | Quantity |
|  | U |  | PLATE |  |
|  | V |  | PIN, 4MM x 16L |  |
|  | W |  | SPRING |  |
|  | X |  | SET SCREW, M6 x 10L |  |
|  | Y |  | BLOCK |  |
|  | Z |  | RING |  |
| 42 |  | 700479 | DANCER BAR ASSEMBLY | 1 |
|  | V |  | RING |  |
|  | W | 301369 | BEARING HK 1010 |  |
|  | X |  | SWINGING BAR SHAFT |  |
|  | Y |  | DANCER BAR ARM |  |
|  | Z |  | DANCER BAR ROLLER ASSEMBLY |  |
| 47 |  | 500771 | SUPPORT BRACKET | 1 |
| 48 |  | 700466 | FILM HOLDER ASSEMBLY | 1 |
|  | O | 300026 | BEARING, NTB1730 |  |
|  | P | 200078 | SHCS, M6 x 16L |  |
|  | Q | 500474 | THRUST BUSHING,UPPER |  |
|  | R |  | FILM CORE HOLDER (UPPER) |  |
|  | S |  | THRUST BUSHING, LOWER |  |
|  | T |  | FILM HOLDER SHAFT |  |
|  | U |  | CLAMP COLLAR |  |
|  | V |  | SPRING SEAT |  |
|  | W | 500113 | SPRING |  |
|  | X |  | FILM CORE HOLDER (LOWER) |  |
|  | Y | 500694 | BRAKE DISC |  |
|  | Z | 500695 | FRICTION SEAT |  |
| 60 |  | 700476 | ROLLER ASS’Y, REAR | 1 |
| 61 |  | 500772 | LIMIT SWITCH MOUNT BRACKET | 1 |
| 62 |  | 400639 | LIMIT SWITCH, TZ-8108 | 2 |
| 63 |  | 500773 | CARRIAGE PLATE, REAR | 1 |
| 64 |  | 500666 | ACRYLIC COVER | 1 |
| 65 |  | 600181 | TERMINAL COVER | 1 |
| 66 |  | 500698 | SPACER, SMALL | 2 |
| 67 |  | 700481 | BEARING SEAT ASSEMBLY | 4 |
|  | X |  | SNAP RING, 42mm, INTERNAL |  |
|  | Y |  | BEARING |  |
|  | Z |  | BEARING SEAT |  |
| 70 |  | 500700 | PROTECTION RING | 1 |
| 71 |  | 600098 | PRE-STRETCH ROLLER, LARGE | 1 |
| 72 |  | 300009 | SNAP RING, 17mm, EXTERNAL | 2 |
| 73 |  | 500699 | SPACER, LARGE | 1 |
| 74 |  | 600099 | PRE-STRETCH ROLLER, SMALL | 1 |
| 75 |  | 600182 | CARRIAGE FRAME | 1 |
| 76 |  | 500677 | SENSOR PLUNGER | 1 |
| No. | Sub No. | Part Number | Description | Quantity |
| 77 |  | 500678 | SECURITY PAN SHAFT | 1 |
| 78 |  | 600183 | FOOT SECURITY PAN | 1 |
| 79 |  | 200084 | SHCS, M8 x 20L | 1 |
| 80 |  | 301360 | HINGE, CARRIAGE DOOR | 2 |
| 81 |  | 200078 | SHCS, M6 x 16L | 1 |
| 82 |  | 500676 | SAFE PLATE | 1 |
| 83 |  | 301363 | LINEAR BUSHING | 1 |
| 84 |  | 500669 | LIMIT SWITCH BRACE | 2 |
| 85 |  | 400671 | LIMIT SWITCH – ARM STYLE | 2 |
| 86 |  | 500048 | BLOCK | 2 |
| 87 |  | 700477 | ROLLER ASS’Y, FRONT | 1 |
| 97 |  | 700505 | ROLLER ASS’Y | 2 |
| 98 |  | 500679 | BACKING NUT | 1 |
| 99 |  | 400643 | PHOTO SENSOR, A3R-2MX | 1 |
| 100 |  | 500680 | PHOTO EYE BRACKET | 1 |
| 101 |  | 301362 | HANDLE, PHOTO EYE BRACKET | 1 |
| 102 |  | 500681 | PHOTO SENSOR SLIDE PLATE | 1 |
| 103 |  | 600184 | SAFETY DOOR | 1 |
| 104 |  | 301364 | SPRING | 1 |
| 105 |  | 500682 | DOOR LOCK BOLT | 1 |
| 106 |  | 700475 | ROLLER ASS’Y, DOOR – INNER | 1 |
| 107 |  | 500683 | LOCK MOUNT PLATE | 1 |
| 108 |  | 200634 | FHCS, M6 x 10L | 1 |
| 109 |  | 500057 | SECURITY KEY | 1 |
| 110 |  | 500667 | HANDLE BAR | 1 |
| 111 |  | 301361 | KNOB, DOOR LOCK | 1 |
| 112 |  | 700482 | CLUTCH ROLLER ASSEMBLY | 1 |
|  | V | 500702 | CLUTCH ROLLER BRKT |  |
|  | W | 301369 | CLUTCHING BEARING, HK1010 |  |
|  | X |  | CLUTCH ROLLER |  |
|  | Y | 301370 | CLUTCHING BEARING, HK 1012 |  |
|  | Z | 500704 | CLUTCH ROLLER BRKT |  |

Optional Film Finger Assembly

Control Box Assembly

Control Box Parts List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

Parts available in inventory are highlighted. Non-highlighted parts may have longer lead times.

| No. | Sub No. | Part Number | Description | Quantity |
| --- | --- | --- | --- | --- |
| 1 |  | 600152 | SUPPORT BRACKET | 2 |
| 2 |  | 600153 | MOUNT BRACKET | 2 |
| 3 |  | 200086 | SHCS, M8 x 40L | 8 |
| 4 |  | 600154 | ELECTRICAL BOX | 1 |
| 5 |  | 500106 | HINGE | 2 |
| 6 |  | 500479 | SUBPANEL | 1 |
| 7 |  | 300048 | LOCK PLATE | 2 |
| 8 |  | 600155 | ELECTRICAL BOX DOOR | 1 |
| 9 |  | 306532 | LOCK, W/ KEY | 2 |
| 10 |  | 200124 | PHILLIPS SCREW, M4 x 25L | 1 |
| 11 |  | 500080 | KEY, SAFETY SWITCH | 1 |
| 12 |  | 500016 | SPRING | 2 |
| 13 |  | 200788 | NUT, NYLOC, M4 | 2 |
| 14 |  | 200106 | MACHINE SCREW, M4 x 35L | 4 |
| 15 |  | 400644 | SAFETY SWITCH | 1 |
| 16 |  | 200101 | MACHINE SCREW, M4 x 12L | 2 |
| 17 |  | 500105 | SECURITY SWITCH BRACKET | 1 |

Pneumatic Drawings

Pneumatic Part List

Note

Although all parts are shown in the part list, some may not be available individually. Selected parts must be purchased in assembly.

| No. | Sub No. | Part Number | Description | Quantity |
| --- | --- | --- | --- | --- |
| 1 |  | 301564 | CYLINDER, JAW PIVOT, MCMA-15-16*75 | 2 |
| 2 |  | 304962 | CYLINDER, WIPER TAIL, MCQV-11-40*65M | 1 |
| 3 |  | 306005 | CYLINDER, WIPER PIVOT, MCMA-11-32*250 | 1 |
| 4 |  | 300897 | SOLENOID VALVE, SGL SOL, 24 VDC | 4 |
| 5 |  | 300894 | AIR FILTER REGULATOR UNIT | 1 |
| 6 |  | 304252 | QUICK CONNECTOR | 1 |
| 7 |  | 304251 | QUICK CONNECTOR | 1 |
| 8 |  | 301565 | FLOW CONTROL, 90 DEG. | 2 |
| 9 |  | 301566 | MAGNETIC REED SWITCH, 3M | 3 |
| 10 |  | 301567 | CONNECTOR, L602 w/ NUT | 9 |
| 11 |  | 304256 | CONNECTOR, PL6-02 | 5 |
| 12 |  | 300900 | BRASS SILENCER, MSL-S-01 | 7 |
| 13 |  | 301569 | BRASS SILENCER, MSL-S-M5 | 2 |
| 14 |  | 301570 | FLOW CONTROL, INLINE, 6mm | 1 |
| 15 |  | 301571 | CONNECTOR, TEE, PE-6 | 1 |
| 16 |  | 300908 | PLUG, 1/4" NPT | 1 |
| 17 |  | 303689 | ROTARY FITTING, 6MM TUBE x 6MM THD. | 2 |
| 18 |  | 304963 | SWITCH MOUNT, B32/40 | 1 |
| 19 |  | 301573 | SWITCH MOUNT, B32 | 2 |
| 20 |  | 301574 | CONNECTOR, PU6 | 3 |
| 21 |  | 304302 | FITTING, ELBOW, 6MM TUBE x 5MM THD. | 2 |
| 22 |  | 301575 | CONNECTOR, E-6 | 3 |
| 23 |  | 304964 | FLOW CONTROL – INLINE | 1 |
| 24 |  | 304965 | FLOW CONTROL – 90 DEGREE | 2 |

8

Highlight Industries, Inc.

Predator Platinum Turntable Stretch Wrapper Operation Manual

Notes

# Text boxes

DISCONNECT/

POWER ON

E-STOP

TURNTABLE

SPEED

FILM FORCE

CARRIAGE/

ELEVATOR

SPEED

STOP

RESET

TOUCH PANEL

START